The Contracting Entity:

JAVNO PODJETJE ENERGETIKA LJUBLJANA d.o.o.

Verovškova ulica 62

1000 Ljubljana

Acting under powers delegated, this public procurement conducts:

JAVNI HOLDING Ljubljana, d.o.o.

Verovškova ulica 70

1000 Ljubljana

Number: JPE-RAZ-399/17

TENDER DOCUMENTS

FOR AWARDING A PUBLIC CONTRACT UNDER COMPETITIVE DIALOGUE PROCEDURE

»SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1«

VOLUME P - APPLICATION

Ljubljana, October 2017

# INVITATION TO SUBMIT APPLICATION

JAVNI HOLDING Ljubljana, d.o.o., Verovškova ulica 70, Ljubljana, on the basis of powers delegated by JAVNO PODJETJA ENERGETIKA LJUBLJANA d.o.o., Verovškova ulica 62, 1000 Ljubljana No. JPE-RAZ-399/17 dated 19 October 2017

hereby invites

all interested economic operators to submit their applications in accordance with the requirements of the tender documents for awarding a public contract for the:

» SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1«

The documentation for awarding the public contract (hereinafter also referred to as: Volume P, tender documents, other contract award documentation) specifies the conditions and requirements for the selection of qualified economic operators who will participate and the dialogue in the narrow sense, and criteria of the Contracting Entity for the selection of the most economically advantageous tenderer who will be awarded the contract.

The tender documents also include possible changes, amendments and clarifications of tender documents, and answers to questions of economic operators.

Sincerely Yours,

Zdenka GROZDE, univ. grad. iur.

General Manager

- GENERAL PROVISIONS

  - Information about the Contracting Entity

The Contracting Entity awarding the public contract is JAVNO PODJETJE ENERGETIKA LJUBLJANA d.o.o., Verovškova ulica 62, 1000 Ljubljana, which by powers No. JPE-RAZ-399/17 dated 19 October 2017, delegated the execution of the public contract award procedure for the »SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1« to JAVNI HOLDING Ljubljana, d.o.o., Verovškova ulica 70, 1000 Ljubljana. However, the Contracting Entity will sign the contract with the selected tenderer.

    - Definitions

Economic operator means any natural or legal person or group of such persons, including any temporary association of undertakings, which offers the execution of works, the supply of products or the provision of services on the market or in procurement procedures. Economic operator means an independent candidate participating on its own, candidates in a joint application, a tenderer participating on its own, tenderers in a joint tender and designated subcontractors, and other forms of entities permitted and in accordance with the Public Procurement Act (ZJN-3).

A candidate is any economic operator who, on the basis of the published notice of the public contract duly and on time submitted the application for participation in competitive dialogue and attached to its application the information for qualitative selection that is requested by the Contracting Entity.

The tenderer is the candidate who, after the completed phase of the dialogue in the narrow sense, is invited to submit the tender.

  - Subject of public contract

The subject of the public contract is the supply and installation of two (2) gas turbo generator sets and two (2) heat recovery steam generators for the Combined Cycle Power Plant Toplarna Ljubljana – LOT 1, comprising the supply, installation, start-up of the gas turbine and of the heat recovery steam generator and associated equipment, including all the necessary construction works and pipeline connections to the steam turbine and to the contact points with the existing devices.

### Offering long-term servicing of gas turbo generator sets by the manufacturer of gas turbo generator sets – LTSA (two major inspection cycles, with the possibility of termination after the first cycle) will also be an integral part of the tender.

An integral part of the tender is also the supply of a 6V diesel generator to provide the black start of the gas turbine.

Supply and services are put out to tender on turnkey basis within certain supply limit according to FIDIC Conditions of Contract, Silver Book.

    - Interest/ability of the economic operator to finance the project (LOT 1) and the natural gas supply

Prior to the invitation to dialogue, the Contracting Entity wishes to check whether the economic operators have interest/ability to finance the project (LOT 1) and/or natural gas supply in the framework of this public contract. Economic operators must indicate in their application whether or not they are interested in this option (Annex 2/1-2/2). On the basis of this information, the Contracting Entity will decide whether the financing of the project (LOT 1) and / or natural gas supply, as an option, will be included in the public contract. In this case, all conditions and requirements applying to each option will be defined in the invitation to dialogue, including the reasons for exclusion and the conditions for participation of the economic operators, which the candidate with the recognized capability will designate as subcontractors for each separate option.

  - Technical description of the subject of the public contract

The Contracting Entity has prepared a framework description of the subject of the public contract, which comprises the supply of LOT 1, that is the supply of the main technological equipment. The description is indicative, the selected economic operator will have to supply equipment and perform services to ensure safety and security, functionality and reliability of the Gas and Steam Unit.

    - Supply and services

a)	Two gas generator sets with associated equipment and building:

- two gas turbines with reduction gear and generator, capable of operating on primary fuel (natural gas) and secondary fuel (light fuel oil)

- intake and filtering of combustion air

- flue gas exhaust duct towards HRSG, including the bypass stack (if needed)

- system of lubrication and control oil

- anti-noise enclosure of the turbo generator set with a ventilation system

- natural gas supply system inside Gas and Steam Unit building of the Heating Plant Ljubljana (PPE-TOL), including gas filters; including compressor station, if needed (the Contracting Entity provides minimum natural gas pressure of 29 bar(g)

- system for light fuel oil supply system inside Gas and Steam Unit building of the Heating Plant Ljubljana including a high-pressure pumping station

- system for reducing the NOx emissions at the gas turbine (if needed)

- system for washing the compressor and the gas turbine

- system for fire and explosion protection in explosive zones

- electrical equipment of the gas turbo generator set (measurements, protection and control system, which will enable connectivity with the existing control system of the  Contracting Entity, based on the Siemens control system)

- gas unit auxiliary supply system(6 kV switchgear with connection cables, 0.4 kV distribution, DC and uninterrupted power supply system, 0,4 kV diesel generator set)

- black start diesel generator set – 6kV diesel generator for start-up of the gas turbine from no-voltage condition

- 110 kV field for new gas unit in the gas-insulated switchgear (GIS) with measurements and control, including the integration of control in the 110 kV control system at the TE-TOL Unit level

- 110 kV connections between block transformers and the 110 kV switchgear

- construction of the complete gas turbo generator set building, including foundations and electrical installations

- ventilation, cooling and heating of the building

- adequate noise protection of all noise sources

- landscape arrangement of the plateau for the Gas and Steam Unit of the Heating Plant Ljubljana (PPE-TOL)

b)	Two two-pressure heat recovery steam generators with associated equipment and building:

- pressure part of the heat recovery steam generator with water heater for district heating

- steel construction of the heat recovery steam generator with stack

- feedwater tank with deaerator

- feedwater and booster pumps and pumps for district heating

- pipelines with fittings in the heat recovery steam generator building

- auxiliary systems of the heat recovery steam generator

- electrical equipment of the heat recovery steam generator (measurements, protection and control system, which will enable connectivity with the existing control system of the  Contracting Entity, based on the Siemens control system)

- HRSG auxiliary supply system (6 kV switchgear with connection cables , 0.4 kV distribution, system of DC and uninterrupted power supply system)

- construction of the complete HRSG building, including foundations and electrical installations

- ventilation, cooling and heating of the building

- adequate noise protection of all noise sources

c)	Pipe connections and associated equipment:

- high-pressure steam piping

- intermediate-pressure steam piping

- pipelines for HP steam pressure reduction

- low-pressure steam piping for the feedwater tank of the heat recovery steam generator

- condensate pipeline

- pipeline for district heating - feed and return

- secondary cooling system: heat exchangers, pumps, pipelines for cooling water - feed and return

- cold demineralized water pipeline

- warm demineralized water pipeline with pumps

- pipeline for emptying of condensate tank

- HP feedwater pipeline for pressure reducing and desuperheating stations

- low-pressure steam piping for connecting the low pressure heater LCC40-2

- steam piping for turbine consumption, 8.5 bar

- low-pressure steam piping for tank ZD2 and heater LCC40-1

d)	Pressure reducing and cooling stations

- pressure reducing and cooling station, 95/9 bar

- pressure reducing and cooling station, 9/2.5 bar

e)	Services

The associated services are the following:

- project management (reporting, attending coordination meetings, monitoring and adjusting the time schedule, etc.)

- technical coordination at the supply limits

- development of the technologal concept design of the entire Gas and Steam Unit of the Heating Plant Ljubljana (PPE-TOL)

- production of design documentation

- production of a 3D model of the project (e.g.: in BIM technology, etc.)

- insurance of works, equipment and personnel of the contractor, insurance of liability for injuries to persons and damage to property

- transport and temporary storage of the equipment on the construction site

- supervision of construction

- erection/installation of the supplied equipment and erection/installation supervision

- start-up tests and trial operation

- performance of warranty measurements

- quality assurance

- training of operating and maintenance personnel of the Contracting Entity

- production of instructions for operation and maintenance.

    - Long-term servicing of gas turbo generator sets (LTSA)

### Offering of long-term servicing of gas turbo generator sets by the manufacturer of gas turbo generator sets (LTSA) will be an integral part of the tender.

### The Contracting Entity will enter into a Long-term Service Agreement (LTSA) with the manufacturer of the gas turbo generator set given in the tender (regardless of whether the manufacturer of the gas turbo generator set is the tenderer, partner within a tender or a subcontractor).

  - Presentation of the Combined Cycle Power Plant Toplarna Ljubljana (PPE TOL)

The Contracting Entity will construct a new Combined Cycle Power Plant (PPE) for the production of heat and power.

The Contracting Entity carry out public procurement for the supply of equipment and the performance of works for the Combined Cycle Power Plant Toplarna Ljubljana (PPE TOL) by lots:

- LOT 1 – Two gas turbo generator sets with heat recovery steam generators: supply, installation, start-up of two gas turbines and heat recovery steam generators with all ancillaryequipment, including all the necessary construction works and pipeline connections to the battery limits at existing steam turbine and existing plant. A part of the supply in LOT 1 is also the black start diesel generator set – a 6kV diesel generator set to start-up the gas turbine from the no-voltage condition. 110 kV field for new gas unit in the gas-insulated switchgear (GIS) with measurements and control, including the integration of control in the control system at the TE-TOL Unit level, 110 kV connections between block transformers and the 110 kV switchgear.

- LOT 2 – Steam turbo generator set: a new steam turbo generator set has not been foreseen; therefore, the Contracting Entity for the LOT will not carry out a public contract procedure. The existing steam turbo generator set was refurbished in 2016;

- LOT 3 – Fuel supply: reconstruction of the existing heavy fuel oil tanks for storing extra light fuel oil, erection of pumping-over stations and execution of oil-piping and gas-piping connections from the measuring reduction station (MRP) to the Combined Cycle Power Plant Toplarna Ljubljana (PPE TOL);

- LOT 4 – Construction works: comprises all the remaining minor construction works apart from those already included in LOT 1;

- LOT 5 – Power transformers: supply and installation of all transformers;

- LOT 6 – Electrical equipment: the remaining electrical equipment not yet included in  LOTs 1, 5 and 7);

- LOT 7 – Control system of the power station: comprises the integration of control systems of the existing production units, the power control system of the TE-TOL Unit and secondary regulation (system for production control, superior to all other systems) with the control system of the new gas turbines and heat recovery steam generators,

- LOT 8 - Diesel generator: 6kV diesel generator for start-up of the gas turbine from no-voltage condition. This LOT is included in LOT 1.

Two gas generator sets with electrical power output of approx. 2x50 MWe will be erected, each with its own heat recovery steam generator and bypass stack (or with the technology of the once through heat recovery steam generator (OTSG), which allows dry running operation without bypass stack). The connection to the existing steam turbo generator set 2 will be provided. Heavy duty or aeroderivative gas turbines can be used, as far as the technology will meet the technology requirements. The gas turbine can also operate in open cycle, without the heat recovery steam generator, which will allow for a fast start-up within 15 minutes. This will enable the provision of system services – tertiary reserves. The two-pressure heat recovery steam generator, in addition to heating surfaces for the production of steam, also includes a network- water heater as the last heating surface before the exhaust gases enter the stack. This will ensure low temperature of flue gases up to at least 80 0C and a higher energy efficiency, which will be close to 90% in the backpressure regime. The produced steam will be used for electricity production in the existing steam turbine of Unit 2. The main fuel will be natural gas, while extra light fuel oil will be used as reserve. The Contracting Entity guarantees min. pressure of natural gas to be 29 bar(g). Economic operator has to provide adequate input pressure at the inlet into the offered gas turbine and to construct a compressor station, if needed. Operation commencement is foreseen by the end of 2020. The LOT1 equipment of the Gas and Steam Unit of the Heating Plant Ljubljana (PPE TOL) will be located on the west side of the existing production facility of the TE-TOL Unite at the site of the former open-air switchgear in the size of 40m X 70m. The existing steam turbine with generator is located in the existing machine house of the TE-TOL Unit.

FIGURE No. 1 – Attachment to tender documents (in pdf format)

    - Main technical characteristics

  - Two gas turbines with generator

- power output at the generator of the

gas turbo generator set: 		50 MWe ± 6 MWe under ISO conditions (limitation of ratedthermal input of the Gas and Steam Unit (PPE) at the TE-TOL site is 275 MWth)

- fuel: 	natural gas and extra light fuel oil as back-up fuel

- efficiency of gas turbo generator set on

generator terminals: 		≥36 % with natural gas as fuel and under ISO conditions, in compliance with the BAT

- NOx emissions in exhaust gases (at 15% O2):	≤ 30 mg/mn3 with natural gas as fuel

≤ 50 mg/mn3 with extra light fuel oil as fuel

- CO emissions in exhaust gases (at 15% O2):	≤ 30 mg/mn3 with natural gas as fuel

≤ 100 mg/mn3 with extra light fuel oil as fuel

- generator frequency:	50 Hz

- generator voltage:	10.5 kV

- start-up time (100 % power):	max. 15 minutes

The temperature of exhaust gases from the gas turbine must enable the production of steam, as stated under item B. Two heat recovery steam generators; for this purpose supplementary firing may be used in the heat recovery steam generator.

  - Two heat recovery steam generators

- type:		vertical/horizontal

- version:		drum type / once through

- height of the main and bypass stack:	65 m

Steam parameters from the heat recovery steam generator must enable the connection with the existing devices in the TE-TOL Unit.

High-pressure steam

- steam pressure at the gas turbine inlet:	92 bar

- steam temperature at the gas turbine inlet:	520 oC

Intermediate-pressure steam

- steam pressure at the gas turbine inlet	9 bar

- steam temperature at the gas turbine inlet:	250 oC

  - Noise of the gas turbine and of the heat recovery steam generator

- noise emission in the gas turbo generator set and of the heat recovery steam generator building, measured 1 m away from each source: ≤ 82 dB(A) for each individual noise source and ≤ 84 dB(A) in total at any place in the facility;

- noise imission due to the new construction of the Combined Cycle Power Plant Toplarna Ljubljana (under operation of the entire Combined Cycle Power Plant (PPE) – including the steam turbo generator set and/or in case of open cycle operation of gas turbines), measured at the southern boundary of the TE-TOL Unit: ≤ 47 dB(A); measured at the western boundary of the TE-TOL Unit: ≤ 45 dB(A); and/or anywhere on the remaining boundary of the TE-TOL Unit: 63 dB(A), in compliance with Figure 1.4.1-1.

Plan of measuring points for the noise level:

| Measuring point | Location | Limit value |
| --- | --- | --- |
| MM 1 | northern part, at the railway line | 63 dB(A) |
| MM 2 | in front of the residential building at Kajuhova 38, upper floor | 45 dB(A) |
| MM 3 | in the upper floor of the residential building at Toplarniška ulica 7 | 47 dB(A) |
| MM 4 | at the entrance into the residential building at Toplarniška ulica 7, ground floor | 47 dB(A) |
| MM5 | At NW plot boundary of the TE-TOL Unit and towards the building at Ul. Vide Pregarčeve 46 | 45 dB(A) |

Figure 1.4.1-1: Presentation of noise measuring points

  - Fuel data

Natural gas:

- pressure at the LOT1 boundary	29 bar(g)

- lower caloric value		  34 MJ/Sm3

- relative density	     0.5725

- CH4		     98.54 %

- CO2		     0.04 %

- N2 		     0.84 %

- Total S 	     maximum 30 mg/Sm3

Extra light fuel oil:

- caloric value	     42.6 MJ/kg

- density	     860 kg/m3

- sulphur	     maximum 0.10 %

    - Location data

The location for the erection of the main technological equipment lies in the A area, as presented in Drawing 2 - Attachment to tender documents (in pdf format)

The maximum available area for the erection/installation of the equipment is presented in Drawing 2 and is as follows:

- length of the plot	70 m

- width of the plot	40 m

The economic operator will have to protect, remove or relocate existing underground and above ground infrastructure in accordance with the requirements for the construction of the new Gas and Steam Unit (PPE). This also includes the possible removal of industry rail track 3.

Other data on the location:

-	Elevation	288 m

Ambient air conditions:

- maximum summer temperature	+37 °C

- multiannual average temperature in summer (July)	+18,9 °C

- relative humidity (summer)	~ 65 %

- minimum winter temperature 	-20 °C

- multi-year average temperature in winter (January)	-0,8 °C

- relative humidity (winter)	~ 40 %

  - Tender documents for the preparation of application and tender

Tender documents for the preparation of application and tender for the SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1 consists of four volumes:

- Volume P: application

- Volume 1: General part

- Volume 2: Technical part

- Volume 3: Contract

  - Public contract award procedure

The Contracting Entity carries out the public contract under a competitive dialogue procedure in accordance with Article 42 of the Public Procurement Act (ZJN-3).

The awarding of the public contract will be conducted in several stages, as follows:

  - QUALIFICATION STAGE:

After the calling for competition, the Contracting Entity will publish tender documents »Volume P - Application«. Interested economic operators will submit their applications on the basis of tender documents (information for qualitative selection). Based on the received application, the Contracting Entity recognise qualification to economic operators, provided that they meet the conditions and requirements of tender documents.

The Contracting Entity will grant economic operators the qualification and the status of a candidate on the basis of fulfilling the conditions and/or requirements for granting the qualification from the tender documents.

  - STAGE OF DIALOGUE IN NARROW SENSE:

The Contracting Entity will submit to economic operators who have been granted the qualification the tender documents (invitation to dialogue) comprising: »Volume 1: General part, Volume 2: Technical part and Volume 3: Contract«. On the basis of the received tender documents, the candidates will submit the technical part the tender, the proposed long-term service agreement for the gas turbo generator sets (LTSA), and their comments to the contract. After having reviewed the tenders, the Contracting Entity will invite candidates to separate dialogues, in which the Contracting Entity will in one or more stages of the dialogue identify potential solutions with regard to the needs of the Contracting Entity. In the context of the dialogue, the text of the draft contract will also be harmonized. The Contracting Entity reserves the right to change the content and scope of the project in the course of the dialogue according to the information it will obtain during the dialogue stage with the goal of finalizing the solution. The Contracting Entity ensures to the invited candidates that they will be treated on an equal footing and that it will provide all candidates with the same information as the basis for the submission of tenders. The Contracting Entity also reserves the right during the dialogues stage to reject the candidate for which that stage of the dialogue has proven that the tendered subject fails to meet the needs and requirements of the Contracting Entity, stated in the technical specifications and in the tender documents. The candidate must cooperate with the relevant experts in dialogue to enable them to conduct the dialogue on substantive and all other issues of the subject of the public procurement (technical solutions, functionalities, economic, legal issues, etc.).

  - STAGE OF TENDER SUBMISSION AND NEGOTATIONS, AND FINAL TENDER

Upon completion of the dialogue stage, the Contracting Entity will finalize the final invitation to submit tenders in which it will define the final technical and other requirements in relation to the content of the dialogue it has conducted with the candidates (invitation to submit a harmonized technical part of the tender and a commercial tender). The final invitation to submit tenders will also include a harmonized sample of the contract and a precise definition of the content of the project. Upon receipt of tenders, the The Contracting Entity will verify the fulfillment of the conditions and requirements from the invitation to submit tenders. After reviewing the tenders, the The Contracting Entity will invite the tenderers whose tenders will meet the requirements and conditions to start negotiations. Based on the conducted negotiations, the tenderers will be obliged to submit their final commercial tenders in accordance with results achieved at negotiations. The Contracting Entity will then, on the basis of criteria for the selection of »the most economically advantageous tender«, select the tenderer and award the public contract.

  - Scheduled times in the procedure

The scheduled times are as follows:

- publication of a public tender and tender documents 			October 2017

- submission of application 			November 2017

- awarding the qualification 			December 2017

- invitation to dialogues with tender documents 			January 2018

- submission of general, technical and contractual parts of tenders 		April 2018

- competitive dialogue (dialogue in narrower sense) 			May 2018

- submission of tender (technical and commercial part) 			July 2018

- negotiations and final tenders 			August 2018

- signing of contracts with the most advantageous tenderer 		         September 2018

  - Variant application/tender

The Contracting Entity allows no variant applications/tenders.

  - Legal basis

The public contract is to be carried out in accordance with the provisions of:

- the Public Procurement Act (Official Gazette of the Republic of Slovenia, No. 91/15; hereinafter: the Public Procurement Act (ZJN-3)),

- Legal Protection in Public Procurement Procedures Act (Official Gazette of the Republic of Slovenia Nos.  43/2011, 60/2011 – ZTP-D, 63/2013 and 90/2014 – ZDU-1I; hereinafter: the ZPVPJN),

- Construction Act (Official Gazette of the Republic of Slovenia, No. 102/04 – officially consolidated version, No. 14/05 – corr., 92/05 – Public Roads Act (ZJC-B), 93/05 – Veterinary Compliance Criteria Act (ZVMS, 111/05 – Constitutional Court’s Decision, 126/07, 108/09, 61/10 – Mining Act (ZRud-1), 20/11 – Constitutional Court’s Decision, 57/12, 101/13 – Real Property Tax Act (ZDavNepr), 110/13 and 19/15; hereinafter: the ZGO-1),

- other regulations based on the above stated Act, and applicable legislation related to the subject of the public contract.

  - Language and monetary unit

Public procurement is carried out in Slovene language. The economic operator may submit its application in Slovenian or in English. The candidate can submit its tender (technical and commercial) in Slovenian or in English.

Volume 1 – General part and Volume 3 – Contract are prepared in Slovenian and in English, while Volume 2 – Technical part only in English. In case of doubt (inconsistencies) between the two linguistic versions of Volume 1 and of Volume 3, the Slovene language is used for their linguistic interpretation.

The The Contracting Entity reserves the right to request the candidate/tenderer that certain documents from the application/tender are translated into Slovene at the cost of the candidate/tenderer, insofar as this is necessary for the performance of the evaluation applications/tenders. The The Contracting Entity will inform the candidate/tenderer of the need for translation, and specify the deadline by which it must submit the translation of the document. In case a candidate/tenderer does not submit this translation within the deadline determined by the Contracting Entity, the application/tender will be excluded from further evaluation.

The Contracting Entity reserves the right to decide at its own discretion whether a candidate/tenderer shall submit the translation prepared by a court-sworn interpreter or just a simple (uncertified) translation. The cost of translation is to be borne by the candidate/tenderer.

The competitive dialogue and correspondence with candidates/tenderers will be in Slovene or in English language, depending on the candidate/tenderer.

Financial data shall be stated in euro (EUR) to two (2) decimal places.

  - Additional explanations to economic operators

Interested economic operators may request additional explanations or put questions about tender documents through the Public Procurement Portal no later than nine (9) calendar days before the application submission deadline. Answers and/or explanations will be published on the JAVNI HOLDING Ljubljana, d.o.o. website (http://www.jhl.si/javna-narocila-iz-podjetij) on the same site where the Public Tender Documents have been published, as well as on the Public Procurement Portal no later than six (6) calendar days before the application submission deadline, provided that the request was submitted in due time. The Contracting Entity has no obligation to respond to any requests for explanation or questions submitted in any other way.

  - Obligation of the economic operator to obtain complete information

Regardless of data contained in the tender documents, the economic operator must before the submission of its application mandatory visit the facility of the Contracting Entity in which the public contract will be carried out in order to obtain possible other data/information in relation to their performance under these tender documents. For viewing the place of performance of the public contract before the submission of application, the interested economic operators must contact the The Contracting Entity no later than eight (8) calendar days prior to the deadline for the submission of applications. The Contracting Entity make the visit to the place of performance of the public contract possible, provided that the request was submitted in due time.

Contact person:

JAVNO PODJETJE ENERGETIKA LJUBLJANA d.o.o.

Verovškova ulica 62

SI-1000 Ljubljana

Herman Janež

tel.: +386 1 58 75 301

fax: +386 1 58 75 218

electronic address: herman.janez@energetika-lj.si

Under no circumstances will the Contracting Entity be liable to the economic operator, its staff or authorised representative, visiting the place of performance of the public contract, for any personal injury or loss of property. All costs and other expenses for viewing the place of execution of the contract shall be borne by the economic operator.

The Contracting Entity does not assume any responsibility and liability with regard to any oral information given during the visit of the place of performance of the contract before the submission of application. During the visit, the Contracting Entity will not provide any information that would mean unequal treatment of economic operators.

Regardless of information given in tender documents, the economic operator is obliged to acquire on its own responsibility all information that it would need for the preparation of the application.

The economic operator must submit, as Annex 15, the certificate (issue by the Contracting Entity) on the obligatory inspection of the facility where the subject of the public contract will be carried out.

  - Application

The economic operator may only submit one application, either as his own or as a partner in a joint application (group of economic operators). If an economic operator participates in several applications as partner in a joint application, the Contracting Entity will exclude from the procedure of awarding the public contract all the applications in which the economic operator participates.

    - Application of a candidate participating on its own (sole contractor)

An economic operator may act independently as an engineering firm.

Insofar as an economic operator, acting on its own is not also:

- the designer of the power plant design, it must indicate max. three (3) potential designers of the power plant design,

- the supplier of the heat recovery steam generator, it must indicate max. three (3) potential suppliers of the heat recovery steam generator,

- the supplier gas turbo generator set, it must indicate max. three (3) potential suppliers of the gas turbo generator set.

The supplier is an economic operator who manufactures and supplies the equipment.

In the context of the submission of tender, in addition to the economic operator acting on its own, only those economic operators may participate for the above mentioned works who have demonstrated technical ability for such works in accordance with item 2.2.4.2. These economic operators may participate in applications/tenders as partners in a joint application/tender or as a subcontractor. Other conditions and requirements will be checked by the Contracting Entity at the nomination (at the latest on the submission of the final tender). The Contracting Entity will check the reasons for exclusion on the day of the submission of applications.

Economic operator shall fill in Annex 2/1.

    - Joint application

An application based on the connection of two or more economic operators (joint application) must contain for each partner in a joint application all data required for an independent economic operator, unless otherwise specified in these documents. The lead partner must act as engineering firm.

In case that the group of economic operators has no:

- designer of the power plant design, it must indicate max. three (3) potential designers of the power plant design,

- supplier of heat recovery steam generator, the lead economic operator must name in the application max. three (3) potential suppliers of heat recovery steam generator,

- supplier of gas turbo generator set, the lead economic operator must name in the application max. three (3) potential supplieres gas turbo generator set.

The supplier is an economic operator who manufactures and supplies the equipment.

In the context of the submission of tender, in addition to economic operators in a joint application, only those economic operators may participate for the above mentioned works who have demonstrated technicalno ability in accordance with item 2.2.4.2. These economic operators may participate in applications/tenders as partners in a joint application/tender or as a subcontractor. Other conditions and requirements will be checked by the Contracting Entity at the nomination (at the latest on the submission of the final tender). The Contracting Entity will check the reasons for exclusion on the day of the submission of applications.

In cas that the application is submitted by a group of economic operators, they must also submit a legal act on the joint execution of contract.

The said legal act must exactly specify:

- mutual responsibility of individual members of the group for performing the contract within the group,

- unlimited joint and several liability of the members (partners) of the group do the Contracting Entity with regard to all contract obligations,

- the authorized principal carrier (authorized contractor, i.e. a member of the group as the lead partner) of the performance of contract obligations, with whom the Contracting Entity will communicate and who is in relation to the Contracting authorized to make statements on behalf of all members of the group of economic operators/tenderers,

- the holder of insurance policy in respect of all contract obligations,

- all holders of financial accounts and transactions with an indication of the transaction account through which the contract obligations will be paid,

- provisions in the event of a partner's departure and under what conditions there may be a change of members of the group of tenderers/contractors,

- definition of shares and scope/field of work of partners,

- signatories of the contract (with definition whether all members of the group or just an authorized member are signatories),

- the obligation of the members of the group to regularly inform The Contracting Entity of any changes to the legal act on the joint execution of the contract.

In the context of a joint application, each and every member of the group of economic operators has unlimited joint and several liability to the Contracting Entity. Legal act on joint execution of contract shall be attached as Annex 1/1.

The Contracting Entity allows no change of the lead partner or partner in a joint application, except in the case where another economic operator that meets the originally specified conditions and requirements for participation, and for whom no originally specified reasons for exclusion exist, succeeds in whole or in part the original economic operator after the restructuring of the undertaking, including acquis ion, merger or insolvency.

The Contracting Entity also allows the possibility to add new members of the group in a joint application after the expiration of the deadline for the submission of application, but no later than after the expiration of the deadline for the submission of the final technical and commercial tenders that economic operators submit after the completed dialogue and on the basis of invitation to submit final technical and commercial tenders, provided that an economic operator joins the joint tender stated in the application in accordance with items 1.13.1 and 1.13.2. The additionally added member of the group must meet the conditions and requirements from Chapter 2, on the date specified for the submission of application.

In the event of adding new members of the group in a joint application, the economic operators will have to submit the amended/supplemented legal act on joint acting.

The economic operator shall fill in Annex 2/2.

    - Application with subcontractors

An economic operator my subcontract a part of the public contract. In case that the economic operator will carry out the public contract with subcontractors, it must attach to its application:

- the ESPD form filled in by the subcontractor(s) (Annex 3),

- filled in and signed Form 1 to Annex 3 and/or Form 2 to Annex 3,

- filled in Annex 4/1 Participation of subcontractors,

- the requirement for direct payments, insofar this is required by the subcontractor (Annex 4/2).

The Contracting Entity will reject each subcontractor, if there are reasons for its exclusion under item 2.1 of the tender documents. The economic operator must attach for each individual subcontractor the same evidence about meeting the conditions specified in the preceding sentence, as it has to attach for itself, except with regard to conditions for which the evidence is foreseen to be submitted by the subcontractor itself.

The economic operator, to whom the public contract will be awarded, will be fully responsible to the Contracting Entity for the execution of the awarded contract, regardless of the number of subcontractors.

Should an economic operator not act in accordance with the provisions of Article 94 of the Public Procurement Act (ZJN-3), the Contracting Entity will submit to the National Review Commission a proposal to initiate a minor offence procedure referred to point 2 of Article 112(1) of the Public Procurement Act (ZJN-3).

The Contracting Entity may require that the economic operator awarded the public contract submits the subcontractor contract.

    - Execution of special professional works

The Contracting Entity will request the contractor executing individual sets of works requiring special knowledge (construction, electrical installations, mechanical installations, I & C, installation, etc.), to demonstrate technical, personnel and professional competence in the performance of these works. These fields, as well as the conditions and requirements will be further defined in the tender documents and/or in the invitation to dialogue. The contractor executing such individual sets of works will have to be designated/nominated as subcontractors.

In accordance with the preceding paragraph, the Contracting Entity consequently allows economic operators to nominate subcontractors also after the expiration of the deadline for the submission of application, but no later than until the closing date for the submission of the final technical and commercial tenders that the economic operators will submit after the completed dialogue and on the basis of the invitation to submit the final technical and commercial tenders. Subsequently registered subcontractors will have to meet all the conditions and requirements that apply to the relevant subcontractor and will be defined in the invitation to dialogue.

  - Submission of application

Economic operator bears the entire costs for the preparation and submission of application. The deadline for submission of application is no later than 10:00 a.m. on 24 November 2017 according to local time, regardless of the mode of delivery, at the address:

Javni Holding Ljubljana, d.o.o., Verovškova ulica 70, 1000 Ljubljana.

The application must be delivered in a sealed package (envelope), onto which the economic operator must the filled-in form given in Annex 16.

In case of personal delivery, the application shall be handed over at the above stated address in the mailroom of the Company on the ground floor.

Economic operators may amend or withdraw their applications with a written notice, which must be delivered to the Company’s mailroom before the application submission deadline. In case of withdrawal, the application will be returned to the economic operator unopened. The notice on amending or withdrawing the application must be prepared, sealed, labelled and delivered in the same manner as the application, with the envelope labelled »AMENDMENT OF APPLICATION« or »WITHDRAWAL OF APPLICATION« instead of the word »APPLICATION«.

If the application is not submitted before the deadline for the receipt of applications, it shall be considered late. Any such application will be labelled by the Contracting Entity as a late submission and returned unopened to the economic operator.

  - Public opening of applications

Public opening of applications will take place at 12:00 noon on 24 November 2017 in the ground-floor conference room at the headquarters of Javni Holding Ljubljana, d.o.o., Verovškova ulica 70, 1000 Ljubljana, Slovenia; representatives of economic operators possessing written authorisations for participating at the opening, submitted before the opening (Annex 17) may actively participate in the opening. Participation authorisations are not required of registered Tenderer representatives.

At the public opening of applications, a representative of the Contracting Entity will announce the names of economic operators who have submitted applications. The Contracting Entity will keep minutes on the conduct of the public opening of applications, of which a photocopy will be handed over to the representatives of economic operators participating in the public opening after the completed public opening of applications. If the minutes are not served on economic operators at the very opening of the applications, the Contracting Entity will forward it to the economic operators that submitted the applications no later than within five (5) working days to the electronic address of the contact person of the economic operator, stated in Annex 1.

  - Definition of the procedure and decision on the contract award

The Contracting Entity conducts the public contract award under a competitive dialogue procedure, considering Article 42 of the Public Procurement Act (ZJN-3).

  - Review of applications and invitation to dialogue

In the application for participation in the public procurement procedure, economic operators must enclose information for qualitative selection.

In the event that the application of an economic operator:

- fails to meet all the requirements of the Contracting Entity for qualitative selection,

- fails to meet the conditions of the Contracting Entity for qualitative selection,

the Contracting Entity will exclude such application from participation in the public procurement procedure.

In accordance with Article 42(6) of the Public Procurement Act (ZJN-3), only those economic operators will participate in the dialogue, who will have been recognised qualification and invited to dialogue by the Contracting Entity.

  - Confidentiality of data

The Contracting Entity shall ensure public nature and  confidentiality of data in compliance with Article 35 of the Public Procurement Act (ZJN-3), observing the provisions of the law regulating the protection of personal information, confidential data or companies.

The data reasonably labelled by the economic operator as confidential or as a trade secret in accordance with the Companies Act or the law governing the protection of personal information or confidential data, will only be used for the purposes of the public tender and shall not be made available to anyone outside of the group of people participating in the procurement process. These data shall not be made publicly available either during the process of opening of applications or in any later stage of the procurement procedure or following the procurement procedure. The Contracting Entity shall be made fully responsible for ensuring confidentiality of any data so obtained.

In accordance with Article 35 of the Public Procurement Act (ZJN-3), the Contracting Entity will not disclose the proposed solutions or any other confidential information communicated to him by the candidate in the dialogue without the consent of the participating candidate. This consent need not be general, but must relate to information that the contracting authority intends to provide to other candidates.

  - Legal protection

Economic operators are assured legal protection pursuant to the provisions of the Legal Protection in Public Procurement Procedures Act (ZPVPJN).

Pursuant to the ZPVPJN, a petition for review may be submitted at any stage of the awarding process for public contracts and in response to any action of the Contracting Entity, provided that the law regulating the award of public contracts or the ZPVPJN contain no provisions to the contrary.

If the request for review concerns the contents of the announcement, invitation to submit application or the public tender documents, the applicant is obliged upon submitting the request to pay a fee of EUR 3,500.00 to the bank account IBAN SI56 0110 0100 0358 802, Ref. No. 11 16110-7111290-XXXXXXLL (where the first six digits are the sequential number of the announcement on the Public Procurement Portal entered by the economic operator itself, and the last two digits designate the year in question).

The request for review must comply with the provisions of Article 15 of the Legal Protection in Public Procurement Procedures Act (ZPVPJN) and must be submitted directly to the Contracting Entity, either per registered mail or per registered mail against advice of delivery. Evidence of the tax paid must be attached to the request. The request for review must be submitted within the time limit set in Article 25 of the ZPVPJN.

  - Economic operator not established in the Republic of Slovenia

An economic operator and individual members of the group of economic operators participating in a joint application/tender, who are not established in the Republic of Slovenia, must demonstrate their individual capabilities in accordance with the requirements of the Contracting Entity stated in tender documents, equally applicable to all economic operators, and in accordance with the provisions of Article 77(4) of the Public Procurement Act (ZJN-3); they must attach such evidence to the application/tender.

An economic operator, not established in the Republic of Slovenia, must in Annex 1 (Data on the candidate), name its representative for servicing in the Republic of Slovenia, in accordance with the General Administrative Procedure Act (Official Gazette of the Republic of Slovenia, No. 24/06, as amended; hereinafter: the ZUP-UPB2).

An economic operator and an individual member of the group of economic operators participating in a joint application/tender, who is established outside the Republic of Slovenia, will have to submit on its own all certificates or other means of proof for the qualitative selection, issued by the competent authority from the country of its origin, proving that there are no reason for the exclusion of the economic operator, and proving its fulfilment of participation conditions, insofar the Contracting Entity will not be able to obtain such certificates from the relevant register.

The same applies to other economic operators (e.g. subcontractors), who will be nominated by the economic operator only after the submission of tender (after the completed second stage, i.e. after the dialogue in narrower sense), and are not established in the Republic of Slovenia.

  - Validity of application

The application must remain valid for at least six (6) months from the date specified for the submission of application.

- QUALITATIVE SELECTION

For qualitative selection, the economic operator must fill in, and attach and sign the printed ESPD form, in Annex to these tender documents. The same applies if the economic operator participates with partners (joint application) or subcontractors (a separate ESPD form for itself as the economic operator, and separate ESPD forms for each of the economic operators participating in the application/tender). It is desired that the ESPD form is also attached in electronic form in xml format.

Through the website http://www.enarocanje.si/_ESPD/ the economic operator imports the Contracting Entity’s ESPD form available at the website of the Contracting Entity at the place where the tender documents are published. The economic operator fills it in, prints and signs it,   and attaches it to the application.

The Contracting Entity may at any time durin the procedure call on the economic operators with the request to submit all or part of evidence in relation to the statements made in the ESPD.

The economic operator, not established in the Republic of Slovenia, must prove each separate ability in accordance with the requirements of the Contracting Entity stated in tender documents, which equally apply to all economic operators; in the application, it has to submit all certificates/evidence issued by the competent authority in its country of origin, proving that there are no reason for the exclusion of the economic operator, and proving its fulfilment of participation conditions.

Where a Member State or a third country of the economic operator, not established in the Republic of Slovenia, does not issue documents and certificates referred to in the preceding paragraph, or where these do not cover all the cases specified in paragraphs 1 and 2 and point b) of paragraph 4 and point b) of paragraph 6 of Article 75 of the Public Procurement Act (ZJN-3), they may be replaced by a declaration on oath, or in Member State or a third country where there is no provision for declaration on oath, by a declaration bade by the person concerned before a competent judicial or administrative authority, a notary or a competent professional or trade organisation in the country of origin of this person or in the country where the economic operator is established.

  - Exclusion grounds

Economic operator must meet the required conditions under item 2.1. If an economic operator participates in a joint application, the conditions from item 2.1 of the tender documents must also be met by each member in the group. If the economic operator acts with subcontractors the conditions from item 2.1 of the tender documents must also be met by the designated subcontractor.

A: Grounds relating to criminal convictions

The Contracting Entity will exclude the economic operator from participation in the public procurement procedure if during the verification process pursuant to Articles 77, 79 and 80 of the Public Procurement Act (ZJN-3) it has established or is otherwise made aware, that a final judgement has ever been pronounced against the economic operator or an individual who is in a managing, executive or supervisory position of the economic operator or has powers of representation, decision or control therein has been the subject of conviction if the judgement contains elements of criminal acts laid out in Article 75(1) of the ZJN-3.

Supporting evidence:

The ESPD form (in »Part III: Exclusion Ground, A: Grounds relating to criminal convictions«) filled in by all economic operators in the application.

Economic operator established in the Republic of Slovenia shall attach to the application the authorities to obtain information from the criminal record for itself and for all persons who are members of the economic operator's administrative, managerial or supervisory body or who have powers for its representation or decision-making or control (Form 1 to Annex 3; Form 2 to Annex 3) or certificates  from the relevant registry such as a court register or if no such registry exists, an equivalent document issued by the competent judicial or administrative authority in the Republic of Slovenia, another member state or the country of origin or the country where the economic operator is headquartered. The certificates thus presented must reflect the last state.

The economic operator established outside the Republic of Slovenia must submit in its application a certificate from the criminal record for itself and for all persons who are members of the administrative, managerial or supervisory body of the economic operator, or who have the authority to represent or control it or decide on its behalf or supervise it. If the certificates are not attached, the Contracting Entity will request the economic operator to submit the missing certificates. Economic operators established outside the Republic of Slovenia need not attach the filled-in Form 1 to Annex 3 or Form 2 to Annex 3, as the case may be.

B: Grounds relating to payment of taxes or social security contributions

The Contracting Entity will exclude an economic operator from participation in the public procurement procedure if during the verification process pursuant to Articles 77, 79 and 80 of the Public Procurement Act (ZJN-3) it determines that, pursuant to applicable legislation regulating financial administration, the economic operator has failed to pay mandatory duties and meet other non-tax monetary obligations collected by a tax authority pursuant to the regulations of state where it is headquartered or the state of the Contracting Entity if the value of any such unpaid overdue obligations exceeds EUR 50 on the date of the submission of application. The economic shall also be considered non-compliant with the obligations from the preceding sentence if, on the date of the submission of application it fails to present all statements on withholding tax on income from employment relationships for the five years before the date of the submission of application.

Supporting evidence:

ESPD Form (in »Part III: Exclusion grounds, B: Grounds relating to payment of taxes or social security contributions «) filled-in by all economic operators in the application.

The Contracting Entity will obtain the certificate issued by the competent authority in the Republic of Slovenia or from the eDosje application for economic operators established in the Republic of Slovenia. The candidate established outside the Republic of Slovenia must submit the certificate from as competent authority by itself. If the certificates are not attached, the Contracting Entity will request the economic operator to submit the missing certificates.

D: National grounds for exclusion

The Contracting Entity will exclude an economic operator from the public procurement procedure if:

- if on the date of deadline for the submission of application the economic operator has been removed from public procurement procedures due to its listing in the records of economic operators with negative references;

- if within the last three years before the application submission deadline, the economic operator has ever been fined twice for offences concerning labour compensation pursuant to a final decision issued by a competent authority of the Republic of Slovenia of another Member State or a third country.

Supporting evidence:

ESPD Form (in »Part III: Exclusion grounds, D: Nacional grounds for exclusion«) filled-in by all economic operators in the application.

The Contracting Entity will obtain the certificate issued by the competent authority in the Republic of Slovenia or from the eDosje application for economic operators established in the Republic of Slovenia. The candidate established outside the Republic of Slovenia must submit the certificate from as competent authority by itself. If the certificates are not attached, the Contracting Entity will request the economic operator to submit the missing certificates.

  - Conditions for participation

    - Suitability for pursuing the professional activity

The economic operator must be entered into one of the professional or business registers maintained in the Member State where the economic operator is headquartered. The relevant professional or trade registers in EU Member States are defined in ANNEX XI of DIRECTIVE 2014/24/EU.

If economic operators are required to obtain a certain licence or be a member of a certain organisation in order to perform a certain service in their country of origin, the Contracting Entity may request that they submit proof of such a licence or membership in the course of the public procurement procedure.

The condition must be met by the candidate. In the event of a joint application or application with subcontractors, the condition must be met by each partner or subcontractor for the part for which the member of the group assumes the job.

Supporting evidence:

- ESPD Form (in »Part IV: Conditions for participation, ɑ: Joint statement for all conditions for participation«) filled-in by all economic operators in the application.

- Photocopy of the extract from the registry, in which the economic operator has been entered (Annex 5).

    - Quality and Environmental Management Systems

The economic operator must have implemented a certified quality system (ISO 9000 or equivalent) and an environmental management system (ISO 14000 or equivalent).

Dokazila:

- ESPD Form (in »Part IV: Conditions for participation, ɑ: Joint statement for all conditions for participation«) filled-in by all economic operators in the application.

- Photocopies of certificates for quality and environmental management systems (by all economic operators in the application) (Annex 6).

    - Organisational structure of economic operators and capabilities for the execution of contract obligations

The economic operator and each member of the group must submit a scheme of organisational structure of the company and organizational structure of the (intended) project group (all economic operators listed in the application).

The economic operator must submit an organisational scheme for for those parts of its organisational structure that will implement the concept design of the Comined Cycle Power Plant Toplarna Ljubljana (PPE-TOL), production, construction and testing of individual lots of the Comined Cycle Power Plant Toplarna Ljubljana (PPE-TOL) project.

The economic operator and individual members of the group mustjo their professional qualification and experience of the persons responsible who will be named for the performance of individual specific tasks, as it is evident from the Table below. The economic operator must supply information in the relevant form for each task for the main responsible person and his alternate. Each of the stated responsible persons must the required conditions (experience). CVs of the persons responsible shall also be submitted.

| Task/Position | Total work experience (years) | In CC/CHP GTPP projects (years) | As manager of CC/CHP GTPP projects (years) |
| --- | --- | --- | --- |
| Project manager | 15 | 10 | 4 |
| Project manager (alternate) | 15 | 10 | 4 |
| PPE Design Manager | 15 | 10 | 4 |
| PPE Design Manager (alternate) | 15 | 10 | 4 |
| Site Manager | 15 | 10 | 4 |
| Site Manager (alternate) | 15 | 10 | 4 |

The economic operator must demonstrate that it has a sufficient amount of personnel capabilities to meet current contract obligation and in future agreed and contingent contractual obligations within 30 months of the month of submission of the application. The economic operator must indicate all the aforementioned contract obligations and the involvement of the personnel in the fulfillment of these obligations. Sufficient personnel capabillity means that the economic operator has at least 100 engineers employed and that, in order to meet contract obligations under thie application there must be a total of at least 15 engineers of various required professions available.

Supporting evidence:

- ESPD Form (in »Part IV: Conditions for participation, ɑ: Common statement for all participation conditions«) filled-in by all economic operators in the application.

- Organisational structure scheme (filled-in by all economic operators in the application) (Annex 7/1).

- Organisational structure of the project group (Annex 7/1).

- Professional qualification and experience of responsible persons in the project group (Annex 7/2).

- Description of experience of the responsible person in the project group (Annex 7/3).

- CVs of responsible persons in the project group.

- Sufficient personnel capabillity (Annex 7/4).

    - Technical ability

In the process of application reviewing, the Contracting Entity is entitled to check the reference objects listed in the application. On the request of the Contracting Entity, the candidate is obliged to organize a vizit of the reference object. All costs of the visit of the Contracting Entity’s staff participating the visit will be borne by the Contracting Entity.

The economic operator that submitted individual reference object to prove its technical ability must carry out obligations under the public contract for which it has submitted reference.

      - References of an independent economic operator or the lead economic operator in a joint application

The economic operator must demonstrate that he has successfully carried out turnkey projects (EPCs), which include all engineering of the project, material supply, construction, installation, execution supervision, start-up tests and commissioning of:

- at least three (3) similar projects. A similar project is considered to be a facility that is successfully operating (guaranteed contract values are reached) and has a size of at least 75 MWe, 50 Hz, at least of a type as a Gas Turbine Combined Cycle (GTCC) Unit, which uses for operation a gas turbine with electrical power output of at least 30 MWe, 50 Hz;

- of which at least one (1) reference must be a Gas Turbine Combined Cycle Combined Heat and Power (GTCC CHP) Unit type, which uses for operation a gas turbine with electrical power output of at least 30 MWe, 50 Hz.

The reference facility/plant must be in operation for at least one (1) year with achieved operation reliability of no less that 98%. Reference objects from the period of the last fifteen (15) years will be considered.

References for gas turbines produced under licence will not be recognised.

Only references apply where the reference holder was also the actual contractor.

Supporting evidence:

- ESPD Form (in »Part IV: Conditions for participation, ɑ: Common statement for all participation conditions«) filled in by the economic operator.

- List of references of an independent economic operator or the lead economic operator in a joint application (Annex 8/1).

- References of an independent economic operator or the lead economic operator in a joint application (Annex 8/2).

      - Other references

The economic operator must demonstrate to have experience in the designing and supply of the following sets of equipment in projects of gas and steam units. If an economic operator has no references as a contractor in fact, it must nominate (in accordance with the provisions of items 1.13.1 and 1.13.2) a contractor with appropriate references for the required work as a partner in a joint application or as a subcontractor:

- positive reference as a power plant design manager for at least three (3) similar projects. A similar project is considered to be a facility that is successfully operating (guaranteed contract values are reached) and has a size of at least 75 MWe, 50 Hz, of at least a Gas Turbine Combined Cycle (GTCC) Unit type, which uses for operation a gas turbine with electrical power output of at least 30 MWe, 50 Hz;

- positive reference as supplier of industry or aircraft gas turbine for at least three (3) projects of Gas Turbine Combined Cycle or Gas Turbine Combined Cycle Combined Heat and Power Unit, based on a supplied gas turbine of electrical output between 32 MWe and 56 MWe, 50 Hz,

- positive reference as supplier of the heat recovery steam generator for at least three (3) projects of Gas Turbine Combined Cycle or Gas Turbine Combined Cycle Combined Heat and Power Units, with the supplied heat recovery steam generator of at least 75 t/h with the CE certificate in accordance with the Pressure Equipment Directive (PED),

- positive reference of the gas turbine manufacturer for at least three (3) Long-Term Service Agreements (LTSA) for industry or aircraft gas turbines with electrical output between 32 MWe and 56 MWe, 50 Hz. Only references for completed or on-going agreements with at least one (1) already performed major maintenance cycle will be taken into consideration.

The reference facility/plant must be in operation for at least one (1) year with achieved operation reliability of no less that 98%. Reference objects from the period of the last fifteen (15) years will be considered.

References for gas turbines produced under licence will not be recognised.

Only references apply where the reference holder was also the actual contractor.

The supplier is an economic operator who manufactures and supplies the equipment.

Supporting evidence:

- Filled in ESPD Form (in »Part IV: Conditions for participation, ɑ: Common statement for all participation conditions«).

- List of references of the power plant design manager (Annex 9/1).

- references of the power plant design manager (Annex 9/2).

- List of references of the supplier of industry or aircraft gas turbine (Annex 10/1).

- References of the supplier of industry or aircraft gas turbine (Annex 10/2).

- List of references of the supplier of the heat recovery steam generator (Annex 11/1).

- References of the supplier of the heat recovery steam generator (Annex 11/2).

- List of references of the manufacturer of gas turbines for long-term servicing (Annex 12/1).

- References of the manufacturer of gas turbines for long-term servicing (Annex 12/2).

    - Financial ability

- The economic operator must submit an estimate or projection of financial statements for 2018 and 2019, which show the operating income and expenses, long-term and current assets, capital and obligations. All data must be shown in EUR. If another currency is used, conversion is required based on the valid exchange rate of the currency according to the Bank of Slovenia exchange rate on the day of the publication of the public procurement notice on the Public Procurement Portal of the Republic of Slovenia.

- The economic operator or the lead partner must must demonstrate the availability of or access to liquid assets, loans and other financial resources at least in the amount of EUR 50 million, which corresponds to the scope of the construction of the subject of this public contract in one year, taking into account other contract obligations of the tenderer.

The Contracting Entity reserves the right to verify the given data at the economic operators' banks. For this purpose, an economic and individual member of a group of economic operators must submit information on their banks and on authorized persons with who it will be possible to verify the given data.

- The economic operator must must demonstrate to have achieved more than EUR 120 million of sales revenue in the individual years 2014, 2015 and 2016.

In the event of a joint appearance, the revenues of the economic operator and individualh members in a joint application are totalled. In the event of a joint appearance, the lead economic operator must demonstrate that at least EUR 60 million of sales revenue has been achieved in each of the years 2014, 2015 and 2016. Individual members of the group of economic operators must show that they achieved at least EUR 30 million of sales revenues in each of the years 2014, 2015 and 2016.

- On the basis of the submitted financial statements, the financial ability of an independent economic operator or a lead economic operator in a joint application and of individual members of the group of the economic operator (joint application) is determined. The risk of multiannual loss or insolvency may be the reason for not recognizing the financial ability of the tenderer.

Economic operator (individually, members in a joint application) shall demonstrate financial soundness in the manner that in 2014, 2015 and 2016:

- it did not show a loss,

- the current ratio (the current ratio = short-term assets / short-term liabilities) is not less than 1.0 for each individual year)

- return on equity (ROE = net profit/equity) is at least 4% for each individual year.

To demonstrate its financial ability from item d), the economic operator must meet at least two of the above stated conditions.

Supporting evidence:

- ESPD Form (in »Part IV: Conditions for participation, ɑ: Common statement for all participation conditions«) filled-in by all economic operators in the application.

- Financial ability (Annex 13).

- Photocopies of audited annual reports for 2014, 2015 and 2016 (provided by all economic operators (candidates) in the application) (Annex 13).

    - Fulfillment of contract obligations

The reasons for non-reckognition of qualification are as follows:

- the repetition of disputes or arbitration proceedings (two or more in the last fifteen years) involving an economic operator (economic operator in an independent application, individual member in the joint application and nominated subcontractors) and and such proceedings were resolved in favour of the counterparty,

- non-fulfillment of contract obligations, resulting in a dispute or an arbitration procedure,

- failure to comply with contractually guaranteed parameters resulting in a dispute or an arbitration procedure.

Supporting evidence:

- ESPD form (in »Part IV: Conditions for participation, ɑ: Common statement for all participation conditions«) filled-in by all economic operators in the application.

- Fulfillment of contract obligations (Annex 14).

- QUALIFICATION

After having reviewed and checked the received applications to the dialogue in the narrower sense (in the second stage of the competitive dialogue, see point 1.6 of the tender documents), the Contracting Entity will invite economic operators who will meet the conditions and requirements of these tender documents. Applications of candidates who, on the basis of assessment of information submitted will not meet the requirements and conditions of these tender documents, will be rejected by the Contracting Entity as inadmissible.

- SELECTION OF THE TENDERER AND CRITERION

The Contracting Entity will select as the most economically advantageous the tender that will show the highest net present value of the project in a twenty (20) year period. The calculation of the net present value will take into account the technical characteristics of the offered subject of the public contract, the volume of steam, hot water and electricity production and the related costs and revenues, the scope of the provision of ancillary services, the tender price with payment terms, operating and maintenance costs (including fuel costs), costs of financing, other costs of the Contracting Entity, depreciation, discounting, and costs of capital.

- INSTRUCTION TO ECONOMIC OPERATORS FOR THE PREPARATION OF THE APPLICATION

  - Preparation of the application

The application shall be prepared so that:

- the application contains all the required documents and forms listed in subchapter 5.2 of the tender documents,

- the application is bound is a manner that prevents individual pages or annexes from being subsequently inserted, removed or replaced without visibly damaging the pages,

- the economic operator shall submit the application in a sealed envelope in a manner which makes it possible to check at the opening the application is sealed in the same way as it was submitted,

- the application is signed and stamped in places where this is required.

The economic operator must submt the original and three (3) copies of the application clearly designated as "original" and "copy". In case of any discrepancies between them, the original prevails.

The economic operator must as Annex 2/3 attach to the original application also an electronic medium (USB, CD) containing the electronic copy in PDF format of all documents contained in the application (a SCAN of the entire application with filled-in and signed documents). The ESPD form shall be attached as a separate document in XML format. In case of discrepancies between the printed and electronic form of the application, the Contracting Entity will consider the printed version.

The economic operator must put the original and each copy of the application in separate envelpes, and correctly mark the envelopes as "ORIGINAL APPLICATION" and "COPY No.". These envelopes shall then be inserted in a sealed outer envelope.

Annexes of tender documents to be filled-in by the economic operator are the basis for establishing the completeness of the application and the grounds for qualitative selection of economic operators pursuant to the requirements and conditions of the tender documents. The economic operators are obliged to attach all the required Annexes, unless otherwise stated in an individual Annex.

An integral part of tender documents include any changes, amendments and corrections of the tender documents and additional explanations and answers to questions of economic operators, published on the Public Procurement Portal and on the website http://www.jhl.si/javna-narocila-iz-podjetij, which economic operators must observe when preparing the application.

  - Contents of the application

The application documents required by the Contracting Entity in relation with this public contract is stated below:

| DATA ON THE ECONOMIC OPERATOR | Annex 1 |
| --- | --- |

This Annex needs to be filld-in, signed and stamped If several economic operators submit a joint application, the form of Annex 1 must be copied and filled-in by all economic operators.

| LEGAL ACT ON JOINT EXECUTION OF CONTRACT | Annex 1/1 |
| --- | --- |

In case of a joint application, the legal act on joint execution of contract shall be attached to this Annex.

| APPLICATION OF A CANDIDATE PARTICIPATING ON ITS OWN | Annex 2/1 |
| --- | --- |

The economic operator must fill-in, sign and stamp the application form.

| JOINT APPLICATION | Annex 2/2 |
| --- | --- |

The economic operator must fill-in, sign and stamp the application form.

| ELECTRONIC COPY OF THE APPLICATION | Annex 2/3 |
| --- | --- |

Following this pge, the economic operator shall enclose the electronic medium with an electronic copy of all application documents in PDF form (a scan of the entire application with filled-in and signed application documents). The ESPD form shall be attached as a separate document in XML format.

| ESPD FOR ALL ECONOMIC OPERATORS IN THE APPLICATION | Annex 3 |
| --- | --- |

The economic operator shall print and sign the filled-in ESPD form and attach it to the application. The same applies to other economic operators (economic operators in a joint application, subcontractors), who participate in the submission of the application.

| PARTICIPATION OF A SUBCONTRACTOR | Annex 4/1 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| REQUEST OF A SUBCONTRACTOR FOR DIRECT PAYMENTS | Annex | 4/2 |
| --- | --- | --- |

The economic operator must fill-in, sign and stamp the form.

| SUITABILITY FOR PURSUING THE PROFESSIONAL ACTIVITY | Annex 5 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| QUALITY AND ENVIRONMENTAL MANAGEMENT SYSTEMS | Annex 6 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| ORGANISATIONAL STRUCTURE OF THE ECONOMIC OPERATOR | Annex 7/1 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| PROFESSIONAL QUALIFICATIONS AND EXPERIENCE OF RESPONSIBLE PERSONS IN THE PROJECT GROUP | Annex 7/2 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| DESCRIPTION OF EXPERIENCE OF THE RESPONSIBLE PERSON IN THE PROJECT GROUP | Annex 7/3 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| SUFFICIENT PERSONNEL CAPABILLITY | Annex 7/4 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| LIST OF REFERENCES OF AN INDEPENDENT ECONOMIC OPERATOR OR THE LEAD ECONOMIC OPERATOR IN A JOINT APPLICATION | Annex 8/1 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| REFERENCES OF AN INDEPENDENT ECONOMIC OPERATOR OR THE LEAD ECONOMIC OPERATOR IN A JOINT APPLICATION | Annex 8/2 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| LIST OF REFERENCES OF THE POWER PLANT DESIGN MANAGER | Annex 9/1 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| REFERENCES OF THE POWER PLANT DESIGN MANAGER | Annex 9/2 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| LIST OF REFERENCES OF THE SUPPLIER OF INDUSTRY OR AIRCRAFT GAS TURBINE | Annex 10/1 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| REFERENCES OF THE SUPPLIER OF INDUSTRY OR AIRCRAFT GAS TURBINE | Annex 10/2 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| LIST OF REFERENCES OF THE SUPPLIER OF THE HEAT RECOVERY STEAM GENERATOR | Annex 11/1 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| REFERENCES OF THE SUPPLIER OF THE HEAT RECOVERY STEAM GENERATOR | Annex 11/2 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| LIST OF REFERENCES OF THE MANUFACTURER OF GAS TURBINES FOR LONG-TERM SERVICING | Annex 12/1 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| REFERENCES OF THE MANUFACTURER OF INDUSTRY OR AIRCRAFT GAS TURBINES FOR LONG-TERM SERVICING | Annex 12/2 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| FINANCIAL ABILITY | Annex 13 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| FULFILLMENT OF CONTRACT OBLIGATIONS | Annex 14 |
| --- | --- |

The economic operator must fill-in, sign and stamp the form.

| CERTIFICATE OF THE CONTRACTING ENTITY ON FACILITY INSPECTION | Annex 15 |
| --- | --- |

The economic operator must attach to the application the certificate signed by the Contracting Entity on the inspection of the facility.

| ENVELOPE FORM | Annex 16 |
| --- | --- |

The economic operator must glue this form on the envelope/parcel.

| FORM OF AUTHORISATION FOR PARTICIPATION AT THE PUBLIC OPENING OF APPLICATIONS | Annex 17 |
| --- | --- |

The representative of the economic operator must produce the filled-in form of the authorisation for participation at the public opening of applications to the professional committee of the Contracting Entitya on the day of application opening.

| DATA ON THE ECONOMIC OPERATOR | Annex 1 |
| --- | --- |

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

| Name of the economic operator |  |
| --- | --- |

| Address of the economic operator |  |
| --- | --- |

| Responsible person |  |
| --- | --- |
| Position |  |
| Phone No. |  |
| Fax No. |  |
| E-mail |  |

| Contact person |  |
| --- | --- |
| Position |  |
| Phone No. |  |
| Fax No. |  |
| E-mail |  |

| E-mail for servicing the decision pursuant to Article 90 of the Public Procurement Act (ZJN-3) through the Public Procurement Portal: |  |
| --- | --- |

| Economic operator is an SME* (please tick as appropriate): | Yes | No |
| --- | --- | --- |

*SMEs: micro, small and medium-sized enterprises as defined in Commission Recommendation 2003/361/ES.

| Transaction/business account (IBAN, SWIFT) |  |
| --- | --- |
| Parent bank |  |
| VAT ID number: |  |
| Financial Authority Office |  |
| Registration number |  |
| Authorised servicing representative in the Republic of Slovenia (to be filled-in only by economic operators, not established in the Republic of Slovenia) |  |

| (place, date) | (stamp) | (Name and signature of the economic operator) |
| --- | --- | --- |

Instruction: If several economic operators submit a joint application, the copied forms of Annex 1 muist be filled-in by all members of the group.

| LEGAL ACT ON JOINT EXECUTION OF CONTRACT | Annex 1/1 |
| --- | --- |

LEGAL ACT ON JOINT EXECUTION OF CONTRACT

Following this page, the legal act on joint execution of contract, signed and stamped by all economic operators (joint application) participating in the execution of of the contract.

| APPLICATION OF A CANDIDATE PARTICIPATING ON ITS OWN | Annex 2/1 |
| --- | --- |

APPLICATION No.: _____________ for the public contract No. JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

We submit this application (please tick as appropriate):

| On our own |  | With subcontractors |  |
| --- | --- | --- | --- |

- The designer of the power plant design, supplier of the heat recovery steam generator, gas turbo generator set

Economic operator participating on its own as engineering firm ……………………………………………………………………………………………………………………………………..… (Name of the economic operator) (mark with “x” as appropriate):

- I am the designer of the power plant design,

- I am not the designer of the power plant design; the designer of the power plant design will be:

- ……………………………………………………………………………………. or

- …………………………………………………………………………………….. or

- ……………………………………………………………………………………… .

- I am the supplier of the heat recovery steam generator,

- I am not the supplier of the heat recovery steam generator; the supplier of the heat recovery steam generator will be:

- ……………………………………………………………………………………. or

- …………………………………………………………………………………….. or

- ……………………………………………………………………………………… .

- I am the supplier gas turbo generator set,

- I am no the supplier gas turbo generator set; the supplier gas turbo generator set will be:

- ……………………………………………………………………………………. or

- …………………………………………………………………………………….. or

- ……………………………………………………………………………………..  .

- Interest/ability of the economic operator to finance the project (LOT 1)

Economic operator participating on its own as an engineering firm ……………………………………………………………………………………… (Name of the economic operator) (mark with “x” as appropriate):

- I have interest/ability to finance the project (LOT 1),

- I have no interest/ability to finance the project (LOT 1).

- Interest/ability of the economic operator for natural gas supply

Economic operator participating on its own as an engineering firm ……………………………………………………………………………………… (Name of the economic operator) (mark with “x” as appropriate):

- I have interest/ability for natural gas supply,

- I have no interest/ability for natural gas supply.

- Veljavnost application

Validity of the application expires on ………………………… (state the date!) (at leats six (6) months from the date specified for the submission of the application).

| (place, date) | (stamp) | (Name and signature of the economic operator) |
| --- | --- | --- |

| JOINT APPLICATION | Annex 2/2 |
| --- | --- |

APPLICATION No.: _____________ for the public contract No. JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

We submit this pplication (please tick as appropriate):

| joint application | with subcontractors |  |
| --- | --- | --- |

- The designer of the power plant design, supplier of the heat recovery steam generator, gas turbo generator set

The lead economic operator (the lead partner) as engineering firm in the joint application ………………………………………………………………………………………………………………………………………… (Name of the lead economic operator) together with partners: ……………………………………………………………………………………………………………………………….………. (Names of partners) (mark with “x” as appropriate):

- In the group of partners, the designer of the power plant design is: …………………………………………………………………………………………………. (Name of the partner),

- In the group of partners, we have no designer of the power plant design; the designer of the power plant design will be:

- ……………………………………………………………………………………. or

- …………………………………………………………………………………….. or

- ……………………………………………………………………………………… .

- In the group of partners, the supplier of the heat recovery steam generator is …………………………………………………………………………..………………………. (Name of the partner),

- In the group of partners, we have no supplier of the heat recovery steam generator; the supplier of the heat recovery steam generator will be:

- ……………………………………………………………………………………. or

- …………………………………………………………………………………….. or

- ……………………………………………………………………………………… .

- In the group of partners, the supplier of the gas turbo generator set is ……………………………………………………………………..……………………………. (Name of the partner),

- In the group of partners, we have no supplier of the gas turbo generator set; the supplier of the gas turbo generator set will be:

- ……………………………………………………………………………………. or

- …………………………………………………………………………………….. or

- ……………………………………………………………………………………..  .

- Interest/ability of the economic operator to finance the project (LOT 1)

As a group of economic operators in the joint application (mark with “x” as appropriate):

- We have interest/ability to finance the project (LOT 1),

- We have no interest/ability to finance the project (LOT 1).

- Interest/ability of the economic operator for natural gas supply

As a group of economic operators in the joint application (mark with “x” as appropriate):

- We have interest/ability for natural gas supply,

- We have no interest/ability for natural gas supply.

- VALIDITY OF APPLICATION

Validity of the application expires on ………………………… (state the date!) (at leats six (6) months from the date specified for the submission of the application).

| (place, date) | (stamp) | (Name and signature of the (lead) economic operator) |
| --- | --- | --- |

| ELECTRONIC COPY OF THE APPLICATION | Annex 2/3 |
| --- | --- |

We, the economic operator ______________________________________________________,

submitting the application for the public contract JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1, attach after this page a USB stick with:

- an electronic copy of all application documents in PDF form (a scan of the entire application with filled-in and signed application documents),

- the ESPD form in XML format.

| ESPD FOR ALL ECONOMIC OPERATORS IN THE APPLICATION | Annex 3 |
| --- | --- |

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

The economic operator shall print and sign the filled-in ESPD form and attach it to the application. The same applies to other economic operators (membere and a joint application, subcontractors), who participate in the submission of the application.

Economic operator established in the Republic of Slovenia shall attach to the application the authorities to obtain information from the criminal record for itself and for all persons who are members of the economic operator's administrative, managerial or supervisory body or who have powers for its representation or decision-making or control (Form 1 to Annex 3; Form 2 to Annex 3) or certificates  from the relevant registry such as a court register or if no such registry exists, an equivalent document issued by the competent judicial or administrative authority in the Republic of Slovenia, another member state or the country of origin or the country where the economic operator is headquartered. The certificates thus presented must reflect the last state.

The economic operator established outside the Republic of Slovenia must submit in its application the certificates listed in the subchapter 2.1 The reasons for exclusion, item A, item B and the second indent of item D by itself. Should the certificates not be attached, the Contracting Entity will request the economic operator to submit the missing certificates. The certificates thus presented must reflect the last state.

Where a Member State or a third country of the economic operator, not established in the Republic of Slovenia, does not issue documents and certificates referred to in the preceding paragraph, or where these do not cover all the cases specified in paragraphs 1 and 2 and point b) of paragraph 4 and point b) of paragraph 6 of Article 75 of the Public Procurement Act (ZJN-3), they may be replaced by a declaration on oath, or in Member State or a third country where there is no provision for declaration on oath, by a declaration bade by the person concerned before a competent judicial or administrative authority, a notary or a competent professional or trade organisation in the country of origin of this person or in the country where the economic operator is established.

Form 1 to Annex 3

AUTHORISATION FOR OBTAINING CERTIFICATES FROM CRIMINAL RECORDS

– FOR LEGAL ENTITIES

_________________________________________________________________ We, (name of the authoriser) hereby authorise JAVNI HOLDING Ljubljana, d.o.o., Verovškova ulica 70, 1000 Ljubljana, to obtain from the Ministry of Justice the certificate from the criminal records for the purpose of verifying our fulfilment of conditions in the procedure of awarding the public contract JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1.

Data on legal entity:

Entity’s name: _____________________________________________________________

Entity’s headquarters: _________________________________________________________

Municipality of Entity’s headquarters: _____________________________________________

Number of entry into the Court’s register (Entry No.): ___________________________________________

Registration number of the Entity: _________________________________________________________

| (place, date) | (stamp) | (Name and signature of the economic operator) |
| --- | --- | --- |

Instruction: Economic operators established in the Republic of Slovenia fill-in and sign the Annex and attach it to the application. Economic operators established outside the Republic of Slovenia need not attach the filled-in Form 1 to Annex 3; economic operators must attach the proof of fulfilling the condition in the application.

Form 2 to Annex 3

AUTHORISATION FOR OBTAINING CERTIFICATES FROM CRIMINAL RECORDS

– FOR NATURAL PERSONS

I, the undersigned ___________________________________________________ (full name) hereby authorise JAVNI HOLDING Ljubljana, d.o.o. , Verovškova ulica 70, 1000 LJUBLJANA, to obtain from the Ministry of Justice the certificate from the criminal records for natural persons, for the purpose of verifying our fulfilment of conditions in the procedure of awarding the public contract JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1.

My personal data are as follows:

PIN: _______________________________________________________________________

DATE OF BIRTH: ______________________________________________________________

PLACE OF BIRTH:_______________________________________________________________

MUNICIPALITY OF BIRTH:_____________________________________________________

STATE OF BIRTH: _____________________________________________________________

ADDRESS OF PERMANENT/TEMPORARY RESIDENCE:

- (Street and number) ________________________________

- (Post code and town) ______________________________

CITIZENSHIP: ______________________________________________________________

MY FORMER SURNAME WAS:_____________________________________________

| (place, date) |  | (signature of the authoriser) |
| --- | --- | --- |

Instruction: The authorisation form must be filled-in and signed by persons who are members of an administrative, managerial or supervisory body of an economic operator established in the Republic of Slovenia, or who have powers for its representation or decision-making or control. Persons who are members of an administrative, managerial or supervisory body of an economic operator established outside the Republic of Slovenia, or who have powers for its representation or decision-making or control need not attach Form 2 to Annex 3; the economic operator must attach the evidence that such persons meet the conditions in the application itself.

| PARTICIPATION OF A SUBCONTRACTOR | Annex 4/1 |
| --- | --- |

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

| Name of the subcontractor |  |
| --- | --- |
| Full Address |  |
| In accordance with Article 94 of the Public Procurement Act (ZJN-3) we, as a subcontractor require direct paymentfrom the Contracting Entity | Please tick/circle as appropriate |
|  | YES | NO |
| Each subcontracted part of the public contract (services/construction/goods), (type/description of works) |  |

| (place, date) | stamp | (Name and signature of the subcontractor) |
| --- | --- | --- |
| (place, date) | stamp | (Name and signature of the economic operator) |

Instruction: Please make copies as needed.

| REQUEST OF A SUBCONTRACTOR FOR DIRECT PAYMENTS | Annex | 4/2 |
| --- | --- | --- |

We, the subcontractor___________________________________________________________ (Name of full address of the subcontractor)

Being a subcontractor of the economic operator

__________________________________________________________________

REQUIRE

That the Contracting Entity pays our amounts receivable from the contractor (the economic operator with whom we will cooperate as its subcontractor) in relation with the execution of the public contract No. JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1, directly to our transaction account, and does so on the basis of the issued interim invoices previously confirmed by the contractor and annexed to the invoice or interim invoice issued to the Contracting Entity by the contractor.

| (place, date) | stamp | (Name and signature subcontractor) |
| --- | --- | --- |

Instruction: Please make copies as needed.

Note: Direct payments to the subcontractor are mandatory in cases where the subcontractor requires direct payment and the subcontractor’s request of for direct payments is attached to the application. If a subcontractor does not request direct payments, this Annex is not filled-in and/or need not be attached to the application.

| SUITABILITY FOR PURSUING THE PROFESSIONAL ACTIVITY | Annex 5 |
| --- | --- |

We, the economic operator ______________________________________________________ ,

who submit the application for the public contract JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1, attach after this page a photocopy from the Register in which the economic operator has been entered (by all economic operators in the application).

| (place, date) | (stamp) | (Name and signature of the economic operator) |
| --- | --- | --- |

| Quality and Environmental Management Systems | Annex 6 |
| --- | --- |

We, the economic operator ______________________________________________________ ,

who submit the application for public contract JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1, attach after this page photocopies of certifikates of quality and environmental management systems (by all economic operators in the application).

| (place, date) | (stamp) | (Name and signature of the economic operator) |
| --- | --- | --- |

| ORGANISATIONAL STRUCTURE OF THE ECONOMIC OPERATOR | Annex 7/1 |
| --- | --- |

We, the economic operator _____________________________________________________,

who submit the application for the public contract JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1, attach after this page:

- the organisational structure of the economic operator (by all economic operators in the  application),

- the organisational structure of the (intended) project group (by all economic operators in the  application), an organisational scheme of the economic operator for those parts of its organisational structure, which will carry out the conceptual design of the Combined Cycle Power Plant Toplarna Ljubljana (PPE-TOL), and the production, construction and testing of individual subunits of Combined Cycle Power Plant Toplarna Ljubljana (PPE-TOL) project.

| (place, date) | (stamp) | (Name and signature of the economic operator) |
| --- | --- | --- |

| PROFESSIONAL QUALIFICATIONS AND EXPERIENCE OF RESPONSIBLE PERSONS IN THE PROJECT GROUP | Annex 7/2 |
| --- | --- |

We, the economic operator _____________________________________________________,

who submit the application for the public contract JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1, demonstrate professional qualifications and experience of responsible persons, stated for the performance of individual specific tasks, as as it is shown in the Table below. For each task we give information in the appropriate form both for the main responsible person and his alternate.

| Full name | Employer | Role | Total work experience [years] | Experience in CC/CHP GTPP projects [years] | Experience as CC/CHP GTPP project manager [years] |
| --- | --- | --- | --- | --- | --- |
|  |  | Project manager |  |  |  |
|  |  | Project manager (alternate) |  |  |  |
|  |  | PPE Design Manager |  |  |  |
|  |  | PPE Design Manager (alternate) |  |  |  |
|  |  | Site Manager |  |  |  |
|  |  | Site Manager (alternate) |  |  |  |

The CVs of the responsible person must be submitted together with their to-date work experiences, highlighting the experience in CC/CHP GTPP projects. The descriptions on form Annex 7/2 must be submitted separately for each individual candidate.

| (place, date) | (stamp) | (Name and signature of the economic operator) |
| --- | --- | --- |

| DESCRIPTION OF EXPERIENCE OF THE RESPONSIBLE PERSON IN THE PROJECT GROUP | Annex 7/3 |
| --- | --- |

We, the economic operator _____________________________________________________,

who submit the application for the public contract JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1, hereby give the description of experience of the responsible person.

| Task:[state the task] | Responsible person: [The main responsible or the alternate] |
| --- | --- |
| Information on the responsible person | Name and Surname of the responsible person: | Date of birth: |
|  | Professional experience: [list of professional experiences, adequate with regard to the task foreseen in the context of the application] |
|  | Education: |
|  | Membership in professional organisations: |
| Current employer | Name of the employer: |
|  | Address of the employer: |
|  | Name of the position: | Number of years with the current employer: |
|  | Phone No.: | Contact data of the Personnel Dept.: |
|  | Fax: | e-mail: |

| From month/year to month/year | Company/Organisation | Position/Role in the company | Description of work |
| --- | --- | --- | --- |

List of professional education courses and trainings

| From | To | Name of the course, performed by |
| --- | --- | --- |

List of professional experiences in the last 10 years, chronologically:

Specific technical, organisational and managerial experiences shall be listed, important for the execution of the foreseen task in the context of the application.

| From | To | Company / Project / Location / The Contracting Entity / Task / Important technical and organisational and managerial experiences |
| --- | --- | --- |

I, the undersigned, confirm that the enclosed CV adequately describes me, my qualifications, and my experience. I understand that any presentation of false facts can be a reason for my dismissal from the task for which I have been foreseen.

| (place, date) | (stamp) | (Name and signature of the responsible person) |
| --- | --- | --- |

| SUFFICIENT PERSONNEL CAPABILLITY | Annex 7/4 |
| --- | --- |

We, the economic operator _____________________________________________________,

who submit the application for the public contract JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1, demonstrate sufficien amount of personnel capabilities to meet current contract obligation and in future agreed and contingent contractual obligations within 30 months of the month of submission of the application.

| Professional field | Number of employees | Number of persons engaged in 30 months from the month of the application submission | The foreseen number of persons engaged in the project of application |
| --- | --- | --- | --- |
| Mechanical engineering |  |  |  |
| Elektrotechnology |  |  |  |
| Construction |  |  |  |

| Concluded and anticipated contracts |
| --- |
| Name of the contract | Status of the project | Time of execution [month] | Time foreseen to completion [month] |

| (place, date) | (stamp) | (Name and signature of the economic operator) |
| --- | --- | --- |

| LIST OF REFERENCES OF THE OF AN INDEPENDENT ECONOMIC OPERATOR OR THE LEAD ECONOMIC OPERATOR IN A JOINT APPLICATION | Annex 8/1 |
| --- | --- |

……/…… (No. of copy / No. of all copies)

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

The economic operator or the lead partner in the joint application must demonstrate that it has successfully carried out turnkey projects (EPCs), which include the complete engineering of the project, material supply, construction, installation, execution supervision, start-up tests and commissioning of:

- at least three (3) similar projects in the last 15 years from the deadline for the submission of application. A similar project is considered to be a facility that has been successfully operating (guaranteed contract values are reached) and has a size of at least 75 MWe, 50 Hz, at least of a type as a Gas Turbine Combined Cycle (GTCC) Unit, which uses for operation gas turbines with electrical power output of at least 30 MWe, 50 Hz;

- of which at least one (1) reference must be a Gas Turbine Combined Cycle Combined Heat and Power (GTCC CHP) Unit type, which uses for operation gas turbines with electrical power output of at least 30 MWe, 50 Hz.

| LIST OF REFERENCES |
| --- |
| Name of the project | Location | Type of facility | Scope of work of the economic operator |

| (place, date) | stamp | (Name and signature of the economic operator) |
| --- | --- | --- |

| REFERENCES OF AN INDEPENDENT ECONOMIC OPERATOR OR THE LEAD ECONOMIC OPERATOR IN A JOINT APPLICATION | Annex 8/2 |
| --- | --- |

……/…… (No. of copy / No. of all copies)

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

The candidate or the lead partner in a joint application must must demonstrate that it has successfully carried out turnkey projects (EPCs), which include the complete engineering of the project, material supply, construction, installation, execution supervision, start-up tests and commissioning of:

- at least three (3) similar projects in the last 15 years from the deadline for the submission of application. A similar project is considered to be a facility that has been successfully operating (guaranteed contract values are reached) and has a size of at least 75 MWe, 50 Hz, at least of a type as a Gas Turbine Combined Cycle (GTCC) Unit, which uses for operation gas turbines with electrical power output of at least 30 MWe, 50 Hz;

- of which at least one (1) reference must be a Gas Turbine Combined Cycle Combined Heat and Power (GTCC CHP) Unit type, which uses for operation gas turbines with electrical power output of at least 30 MWe, 50 Hz.

Name and location of the project:

Name and address of the reference Contracting Entity:

Full name of the representative of the referene Contracting Entity:

Phone number and e-mail of the representative of the referene Contracting Entity:

Dectription of the subject of the contract and of the scope of supply and scope of services (description of the project):

Number of workers engaged in the execution of the project:

Period of the execution of the project (date)

Period of operation (date)

Project data: Nominal power capacity (MWe) and heat power (MWt) ISO, type of facility

Project data: Type, number and power of gas turbines

Project data: Type, number and capacity of the heat recovery steam generator

Project data: Type, number and power of gas turbines

Project data: Efficiency (%)

Project data: Reliability (%)

Project data: Availability (%)

| (place, date) | stamp | (Name and signature of the economic operator) |
| --- | --- | --- |

| LIST OF REFERENCES OF THE POWER PLANT DESIGN MANAGER | Annex 9/1 |
| --- | --- |

……/…… (No. of copy / No. of all copies)

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

Economic operator must demonstrate in its application that it has experience in the designing and supply of the following sets of equipment in gas and steam unit projects in the last fifteen (15) years until the date set for the submission of application. If the economic operator has no references as the actual provider of works, the requirements can be met together with a partner in a joint application or todether with a designated subcontractor. The economic operator must submit:

- a positive reference as the designer of the power plant design for at least three (3) similar projects. A similar project is considered to be a facility that has been successfully operating (guaranteed contract values are reached) and has a size of at least 75 MWe, 50 Hz, at least of a type as a Gas Turbine Combined Cycle (GTCC) Unit, which uses for operation gas turbines with electrical power output of at least 30 MWe, 50 Hz

| LIST OF REFERENCES |
| --- |
| Name of the project | Location | Type of facility | Scope of work of the economic operator |

| (place, date) | stamp | (Name and signature of the economic operator) |
| --- | --- | --- |

| REFERENCES OF THE POWER PLANT DESIGN MANAGER | Annex 9/2 |
| --- | --- |

……/…… (No. of copy / No. of all copies)

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

Economic operator must demonstrate in its application that it has experience in the designing and supply of the following sets of equipment in gas and steam unit projects in the last fifteen (15) years until the date set for the submission of application. If the economic operator has no references as the actual provider of works, the requirements can be met together with a partner in a joint application or todether with a designated subcontractor. The economic operator must submit:

- a positive reference as the designer of the power plant design for at least three (3) similar projects. A similar project is considered to be a facility that has been successfully operating (guaranteed contract values are reached) and has a size of at least 75 MWe, 50 Hz, at least of a type as a Gas Turbine Combined Cycle (GTCC) Unit, which uses for operation gas turbines with electrical power output of at least 30 MWe, 50 Hz

Name and location of the project:

Name and address of the reference Contracting Entity:

Full name of the representative of the referene Contracting Entity:

Phone number and e-mail of the representative of the referene Contracting Entity:

Dectription of the subject of the contract and of the scope of supply and scope of services (description of the project):

Period of the execution of the project (date)

Period of operation (date)

Project data: Nominal power capacity (MWe) and heat power (MWt) ISO, type of facility

Project data: Type, number and power of gas turbines

Project data: Type, number and capacity of the heat recovery steam generator

Project data: Efficiency (%)

Project data: Reliability (%)

Project data: Availability (%)

| (place, date) | stamp | (Name and signature candidate) |
| --- | --- | --- |

| LIST OF REFERENCES OF THE SUPPLIER OF INDUSTRY OR AIRCRAFT GAS TURBINE | Annex 10/1 |
| --- | --- |

……/…… (No. of copy / No. of all copies)

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

Economic operator must demonstrate in its application that it has experience in the designing and supply of the following sets of equipment in gas and steam unit projects in the last fifteen (15) years until the date set for the submission of application. If the economic operator has no references as the actual provider of works, the requirements can be met together with a partner in a joint application or todether with a designated subcontractor. The economic operator must submit:

- a positive reference as supplier of industry or aircraft gas turbine for at least three (3) projects of Gas Turbine Combined Cycle (GTCC) or Gas Turbine Combined Cycle Combined Heat and Power (GTCC CHP) Units, where the supplied gas turbine had electrical output betweent 32 MWe and 56 MWe, 50 Hz.

| LIST OF REFERENCES |
| --- |
| Name of the project | Location | Type of facility | Scope of work of the economic operator |

| (place, date) | stamp | (Name and signature of the economic operator) |
| --- | --- | --- |

| REFERENCES OF THE SUPPLIER OF INDUSTRY OR AIRCRAFT GAS TURBINE | Annex 10/2 |
| --- | --- |

……/…… (No. of copy / No. of all copies)

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

Economic operator must demonstrate in its application that it has experience in the designing and supply of the following sets of equipment in gas and steam unit projects in the last fifteen (15) years until the date set for the submission of application. If the economic operator has no references as the actual provider of works, the requirements can be met together with a partner in a joint application or todether with a designated subcontractor. The economic operator must submit:

- a positive reference as supplier of industry or aircraft gas turbine for at least three (3) projects of Gas Turbine Combined Cycle (GTCC) or Gas Turbine Combined Cycle Combined Heat and Power (GTCC CHP) Units, where the supplied gas turbine had electrical output betweent 32 MWe and 56 MWe, 50 Hz.

Name and location of the project:

Name and address of the reference Contracting Entity:

Full name of the representative of the referene Contracting Entity:

Phone number and e-mail of the representative of the referene Contracting Entity:

Period of the execution of the project (date)

Period of operation (date)

Achieved number of operating hours

Project data: Nominal power capacity (MWe) ISO, type of facility

Project data: Type, number and power of gas turbines

Project data: Efficiency (%)

Project data: Reliability (%)

Project data: Availability (%)

| (place, date) | stamp | (Name and signature of the economic operator) |
| --- | --- | --- |

| LIST OF REFERENCES OF THE SUPPLIER OF THE HEAT RECOVERY STEAM GENERATOR | Annex 11/1 |
| --- | --- |

……/…… (No. of copy / No. of all copies)

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

Economic operator must demonstrate in its application that it has experience in the designing and supply of the following sets of equipment in gas and steam unit projects in the last fifteen (15) years until the date set for the submission of application. If the economic operator has no references as the actual provider of works, the requirements can be met together with a partner in a joint application or todether with a designated subcontractor. The economic operator must submit:

- a positive reference as supplier of the heat recovery steam generator for at least three (3) projects of Gas Turbine Combined Cycle or Gas Turbine Combined Cycle Combined Heat and Power Units, with the supplied heat recovery steam generator of at least 75 t/h with the CE certificate in accordance with the Pressure Equipment Directive (PED).

| LIST OF REFERENCES |
| --- |
| Name of the project | Location | Type of facility | Scope of work of the economic operator |

| (place, date) | stamp | (Name and signature of the economic operator) |
| --- | --- | --- |

| REFERENCES OF THE SUPPLIER OF THE HEAT RECOVERY STEAM GENERATOR | Annex 11/2 |
| --- | --- |

……/…… (No. of copy / No. of all copies)

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

Economic operator must demonstrate in its application that it has experience in the designing and supply of the following sets of equipment in gas and steam unit projects in the last fifteen (15) years until the date set for the submission of application. If the economic operator has no references as the actual provider of works, the requirements can be met together with a partner in a joint application or todether with a designated subcontractor. The economic operator must submit:

- a positive reference as supplier of the heat recovery steam generator for at least three (3) projects of Gas Turbine Combined Cycle or Gas Turbine Combined Cycle Combined Heat and Power Units, with the supplied heat recovery steam generator of at least 75 t/h with the CE certificate in accordance with the Pressure Equipment Directive (PED).

Name and location of the project:

Name and address of the reference Contracting Entity:

Full name of the representative of the referene Contracting Entity:

Phone number and e-mail of the representative of the referene Contracting Entity:

Description of the subject of contract and scope of supply and scope of services (description of the project):

Number of workers engaged in the execution of the project;

Period of the execution of the project (date)

Period of operation (date)

Project data: Nominal power capacity (MWe) and heat power (MWt) ISO, type of facility

Data on the heat recovery steam generator: (number, type (horisontal/vertical), number of pressure stages (1/2/3) and capacity of the heat recovery steam generator

Project data: Efficiency (%)

Project data: Reliability (%)

Project data: Availability (%)

| (place, date) | stamp | (Name and signature of the economic operator) |
| --- | --- | --- |
| LIST OF REFERENCES OF THE MANUFACTURER OF GAS TURBINES FOR LONG-TERM SERVICING | Annex 12/1 |

……/…… (No. of copy / No. of all copies)

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

Economic operator must demonstrate in its application that it has experience in the designing and supply of the following sets of equipment in gas and steam unit projects in the last fifteen (15) years until the date set for the submission of application. If the economic operator has no references as the actual provider of works, the requirements can be met together with a partner in a joint application or todether with a designated subcontractor. The economic operator must submit:

- positive reference of the gas turbine manufacturer for at least three (3) Long-Term Service Agreements (LTSA) for industry or aircraft gas turbines with electrical output between 32 MWe and 56 MWe, 50 Hz. Only references for completed or on-going agreements with at least one (1) already performed major maintenance cycle will be taken into consideration.

| LIST OF REFERENCES |
| --- |
| Name of the project | Location | Type of facility | Scope of work of the economic operator |

| (place, date) | stamp | (Name and signature of the economic operator) |
| --- | --- | --- |

| REFERENCES OF THE MANUFACTURER OF INUSTRY OR AIRCRAFT GAS TURBINE FOR LONG-TERM SERVICING | Annex 12/2 |
| --- | --- |

……/…… (No. of copy / No. of all copies)

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

Economic operator must demonstrate in its application that it has experience in the designing and supply of the following sets of equipment in gas and steam unit projects in the last fifteen (15) years until the date set for the submission of application. If the economic operator has no references as the actual provider of works, the requirements can be met together with a partner in a joint application or todether with a designated subcontractor. The economic operator must submit:

- positive reference of the gas turbine manufacturer for at least three (3) Long-Term Service Agreements (LTSA) for industry or aircraft gas turbines with electrical output between 32 MWe and 56 MWe, 50 Hz. Only references for completed or on-going agreements with at least one (1) already performed major maintenance cycle will be taken into consideration.

Name and location of the project:

Name and address of the reference Contracting Entity:

Full name of the representative of the referene Contracting Entity:

Phone number and e-mail of the representative of the referene Contracting Entity:

Description of the subject of contract and scope of supply and scope of services (description of the project):

Start of gas turbine operation (date)

Period of operation and period of maintenance/servicing – LTSA (date)

Project data: Nominal power capacity (MWe) and heat power (MWt) ISO, type of facility

Project data: Number, type and power of gas turbines

Project data: Efficiency (%)

Project data: Reliability (%)

Project data: Availability (%)

| (place, date) | stamp | (Name and signature of the economic operator) |
| --- | --- | --- |

| FINANCIAL ABILITY | Annex 13 |
| --- | --- |

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1

The economic operator _____________________________________________________________________________ must demonstrate its financial ability in the application.

Annual financial data

| Financial data | Data for year | Estimated data for year |
| --- | --- | --- |
| A. in EUR | [2014] | [2015] | [2016] | [2018] | [2019] |
| 1. Total assets |  |  |  |  |  |
| 2. Current assets |  |  |  |  |  |
| Long-term assets |  |  |  |  |  |
| Equity |  |  |  |  |  |
| 5. Current and long-term obligations |  |  |  |  |  |
| 6. Profit before taxes |  |  |  |  |  |
| 7. Net profit or loss |  |  |  |  |  |
| 8. Total income |  |  |  |  |  |
| 9. Total expenses |  |  |  |  |  |
| 10. Sales revenue |  |  |  |  |  |
| 10a. of which engineering % |  |  |  |  |  |
| 10b. of which equipment supply % |  |  |  |  |  |
| 10c. of which construction % |  |  |  |  |  |
| 11. Current ratio (current assets/ current obligations) |  |  |  | X | X |
| 12. Return on equity (ROE) (net profit/equity) |  |  |  | X | X |
| 10. EBITDA % |  |  |  | X | X |
|  | Rate of conversion: |
| B. In local currency | [2014] | [2015] | [2016] | [2018] | [2019] |
| 1. Total assets |  |  |  |  |  |
| 2. Current assets |  |  |  |  |  |
| 3. Long-term assets |  |  |  |  |  |
| 4. Equity |  |  |  |  |  |
| 5. Current and long-term obligations |  |  |  |  |  |
| 6. Profit before taxes |  |  |  |  |  |
| 7. Net profit or loss |  |  |  |  |  |
| 8. Toral income |  |  |  |  |  |
| 9. Total expenses |  |  |  |  |  |
| 10. Sales revenue |  |  |  |  |  |
| 10a. of which engineering % |  |  |  |  |  |
| 10b. of which equipment supply % |  |  |  |  |  |
| 10c. of which construction % |  |  |  |  |  |
| 11. Current ratio (current assets/current obligations) |  |  |  | X | X |
| 12. Return on euity (ROE) (net profit/equity) |  |  |  | X | X |
| 10. EBITDA % |  |  |  | X | X |

Attached hereto are audited annual reports for 2014, 2015 and 2016.

Taking into account all the aforementioned contractual obligations, we present the following availability or access to liquid assets, loans or other financial resources of at least EUR 50 million.

| Data on sources of financing |
| --- |
| Source of financing | Amount in EUR | Currency of the economic operator | Rate of concersion | Amount in local currency of the economic operator |

For the conversion into EUR, the valid exchange rate of the currency must be used according to the exchange rate of the Bank of Slovenia on the day of the publication of the notice on the public procurement in the Public Procurement Portal of the Republic of Slovenia.

Data on banks (if the economic operator operates with several banks, the Table below shall be copied and filled-in, as appropriate):

| Bank | Name of the bank: |
| --- | --- |
|  | Address of the bank: |
|  | Phone No.: | Contact person and position: |
|  | Fax: | E-mail: |

By signing this Annex, we agree that the Contracting Entity checks the validity of these statements with banks.

| (place, date) | stamp | (Name and signature of the economic operator) |
| --- | --- | --- |
| FULFILLMENT OF CONTRACT OBLIGATIONS | Annex 14 |

We, the economic operator _____________________________________________________,

who submit the application for the public contract JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1, make this statement on disputes or arbitration procedures in which we were a party to the procedure in relation with non-fulfilment of contract obligations or non-compliance with the guaranteed parameters.

| History of legal disputes |
| --- |
| Year | Contract | The parties involved | Reason/substace of the dispute | Value of the dispute | Outcome of the dispute resolution |

| History of terminations of contracts |
| --- |
| Year | Contract | The parties involved | The reason of termination |

| (place, date) | (stamp) | (Name and signature of the economic operator) |
| --- | --- | --- |

| CERTIFICATE OF THE CONTRACTING ENTITY ON FACILITY INSPECTION | Annex 15 |
| --- | --- |

We, the economic operator _____________________________________________________,

who submit the application for the public contract JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1, attach the certificate of the Contracting Entity on the inspection of the site/facility.

Based on the requirements from tender documents JPE-RAZ-339/17 we confirm that the representative of the economic operator

___________________________________________________________________________

___________________________________________________________________________

(Name of the economic operator)

Represented by: ________________________________________________________________

participated in a meeting and inspection on the site on ………………………………… at …… o’clock.

The meeting was attended by:

___________________________________________	_______________________

(Full name)                                     ( Signature)

Who at the meeting presented the relevant authorisation.

| Ljubljana, |  |  |
| --- | --- | --- |
| (place, date) | stamp | (Signature of the representative of the Contracting Entity) |

| ENVELOPE FORM | Annex 16 |
| --- | --- |

| SUBMITTED BY (Economic Operator): | RECEIPT OF APPLICATION: IN PERSON BY MAIL Date: Hour: Reference number: Sequence number of applications: Copy: |
| --- | --- |

»APPLICATION CODE«

»DO NOT OPEN - APPLICATION:

JPE-RAZ-399/17 - SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1«

Please attach this form on the envelope!

| FORM OF AUTHORISATION FOR PARTICIPATION AT THE PUBLIC OPENING OF APPLICATIONS | Annex 17 |
| --- | --- |

AUTHORISATION

FOR PARTICIPATION AT THE PUBLIC OPENING OF APPLICATIONS

AUTHORISING ENTITY:

___________________________________________________________________________

___________________________________________________________________________

(name and headquarters of the economic operator)

represented by: ________________________________________________________________

AUTHORISES:

___________________________________________________________________________

___________________________________________________________________________

(full name and headquarters of the authorised representative)

___________________________________________________________________________,

(relation to the economic operator)

- to represent the interests of the economic operator at the public opening of applications,

- to actively participate in the public opening process and record any remarks to the contents of the minutes,

- to sign the minutes of the public opening of applications for the contract No. JPE-RAZ-399/17; SUPPLY AND INSTALLATION OF TWO GAS TURBO GENERATOR SETS AND TWO HEAT RECOVERY STEAM GENERATORS FOR THE COMBINED CYCLE POWER PLANT TOPLARNA LJUBLJANA – LOT 1.

| (place, date) | (stamp) | (Name and signature of the economic operator) |
| --- | --- | --- |

# Footnotes

COMMISSION RECOMMENDATION of 6 May 2003 on definition of micro, small and medium-sized enterprises (notified in document No. C(2003) 1422), 2003/361/EC; OJ EU, L 124, 20 May 2003.

# Text boxes

RECIPIENT:

JAVNI HOLDING Ljubljana, d.o.o.

Verovškova ulica 70

1000 LJUBLJANA